## Slide 1
SEC Main
(Schedule Event Controller)
DCS Main
(Device Control System)
DCS Backup
(Device Control System)
IM
(Ingest Manager)
Optional
Broadcast Switcher
Playout Server
RSW
Logo & CG
VCR
Etc
SEC Backup
(Schedule Event Controller)
1. System Diagram – Traditional Automation
SEC (Schedule Event Controller) Creation event schedule & Operation monitoring
DCS (Device Control System) Control broadcasting equipment, check main/backup status and perform automatic switching
IM (Ingest Manager) DCS controls the Video Server to allow material ingest
MCC (Multi Channel Controller) Monitor event and equipment for all channels and SEC status
MCC
(Multi Channel Controller) Optional

## Slide 2
2. Channel in a box System Diagram
SEC
(Schedule Event Controller)
DCS
(Device Control System )
PCS
(Playback Controller)
Master Control Switch
Video Encoder/Decoder
CG – Cut & Page
Sequence CG
Scroll CG
Logo
CC & Subs
Input
PGM
PST
PCS (Playback Control System) Function and control of software broadcasting equipment
Install SEC, DCS, and Playback Controller in one machine
SEC, DCS consist of the same system as the traditional automation
The PCS controls the broadcasting function under the control of the DCS
Minimum 1 input / 1output SDI configuration

## Slide 3
3. PCS Pipeline
VCR or Live
Playback
Primary MEDIA
MIXER
Secondary MEDIA
with DVE
Cut, Page CG
KEYER
LOGO
CC/SUB
VANC
SEQUENCE CG
SCROLL CG
Configuration for at least 1 channel playback
Media playback, CG, Logo, CC / SUB, etc. are developed in software