## Slide 1: Playback Control System
Functional flow block diagram
V 2.0

## Slide 2: Source stream objects
There are several kinds of source stream objects:
  Media device – media file playback, take mode or seamless playback of several files
  Live device – live video+audio input grabbing from some input device
  CG device – one of Character Generator family streams: Cut, Page, Sequence, Scroll, Logo
Number of devices for each category is technically unlimited
Each source object has video and audio output stream. Format of streams is same and set via PCS Settings. This is PCS Output Format.
Each output stream can be connected to other objects in system.
Each output stream can be splitted to connect to several objects and deliver same content to several receivers

## Slide 3: SimpleMixer object
Mixer is an object with several inputs and one output
Each “input” and “output” means video+audio media stream
Output format is PCS Output Format
Each input has such tunable parameters:
  2D position
  2D scale
  Opacity – alpha value
  Some inputs can have alpha channel included in video stream, so they can overlay over bottom image using this info
  Audio gain(volume)
Inputs ordered and overlaid so first is bottom-most, second is over it and so on
Bottom input is a Background. It is always full-sized and only can be turned on or off. Only Media and Live objects can be connected to mixer’s Background input. If Background input is unconnected then it is solid black.
Other inputs also named Keyers
Output stream is a result of compositing of all inputs
Mixer State is a set of all parameters(position, scale, opacity, audio gain) of all inputs
Mixer State can be tuned using PCS UI

## Slide 4: SwitchingMixer object
SwitchingMixer has two Mixer States – two sets of parameters of all inputs and can switch between them using dissolve transition with controllable duration.
Thus possible to set two sets: one for preset output, second for program. And then just to switch between them
State 0
State 1

## Slide 5: ProgramMixer Object
Due to fact that switching between states in SwitchingMixer is possible only with dissolve effect we have to create special object for implementing other transition effects – ProgramMixer
MPlatform can use transition with effects only in MMixer::SetBackground() command. During this command current background stream replaced by next background stream using specified transition effect and duration.
So ProgramMixer consists of two SimpleMixers for two possible states(Current Program and Future Program) and third SimpleMixer that contains only background stream connected to output of one of these state mixer.
State 0
BG Switch
State 1

## Slide 6: Output Device Object
PCS has 4 output device objects: PROGRAM, PRESET, OUTPUT1 and OUTPUT2
Each device uses separate physical output device to stream out video and audio. Configured in PCS Settings
Each Output Device Object has one input stream connector that can be connected to Mixer Object to pass this stream to output device

## Slide 7: Preview Object
Preview Object can connect to any object with output stream
It creates copy of this stream and shows it in preview window in UI

## Slide 8: Functional flow block diagram
Inputs
Preset SwitchingMixer
ProgramMixer
Output 1 SimpleMixer
Output 2 SimpleMixer
PRESET Output
PROGRAM Output
OUTPUT1 Output
OUTPUT1 Output
Input Preview
Preset Preview
Program Preview

## Slide 9: MCS – Master Control Switch commands(5.7)
key_take – For bus(mixer in term of PCS) with “true” sets opacity value for all Keyer inputs as defined in keys array. “True“ – 255, “false” – 0. I.e. here we can turn on/off CGs, logos, etc. separately for all 4 buses. Immediately. Cut effect
crosspoint_take – connects(if true) or disconnects(if false) specified input object as Background for given buses. Immediately. Cut effect
set_enable_key – selects Keyers, whose on/off state is linked(tied) to preset/program background. For example, Keyer1(with CG1) is On for Preset and Off for Program now. Backgrounds are Preset:Media1, Program:Media2. Then we call set_enable_key(Key1=true). And then run AutoTake. We’ll see Media1+CG1 on Program and Media2 on Preset But if we start again from begin but execute set_enable_key(Key1=false) then after AutoTake we will see Media1 on Program and Media2+CG1 on Preview because Keyer1 is not tied to transition and leave on preset bus.
next_transition – is a command to set whether to perform PGM/PST only, key only, or both transitions when executing start_transition command. I understand it so: if background==false, then use Program background for both Preset and Program, regardless crosspoint_take(preset) settings. If key==false, then use current Program key_take settings for both Program and Preset buses regardless key_take(preset) settings