## Slide 1
1. SEC Redundant configuration
SEC #1
(M)
Periodic check of main SEC's alive status.
If main SEC is deadlocked, backup SEC is switch to main.
DCS event is controlled by SEC that is switched to main.
When the previous main SEC is restarted, it operates as a backup.
1.1 SEC redundant workflow
SEC #2
(B)
Alive
Alive check
Alive check
Switch main
Dead
Control event to DCS
Restart &
switch backup

## Slide 2
SEC #1
(M)
DCS #1
(M)
The main SEC sends events to all DCS.
Only the main DCS controls the device for the event.
The main SEC sends the event information to other SEC & MCC.
SEC #2
(B)
DCS #2
(B)
1.2 SEC event input to DCS
Input event
Device
Control
Event information
MCC

## Slide 3
SEC #1
(M)
DCS #1
(M)
SEC receives event status from DCS in two types. 1. Broadcast notify. 2. Only main SEC notify.
The main SEC sends the event status to other SEC & MCC.
SEC #2
(B)
DCS #2
(B)
1.3 SEC receive event status from DCS
Event status broadcast notify
MCC
1. Broadcast notify

## Slide 4
SEC #1
(M)
DCS #1
(M)
SEC #2
(B)
DCS #2
(B)
Event status notify
Event status
MCC
2. Only main SEC notify
The main SEC sends the event status to other SEC & MCC.

## Slide 5
SEC #1
(M)
DCS #1
(M)
SEC check device status from DCS in three types. 1. Broadcast notify. 2. Only controlled SEC notify. 3. Each SEC direct check device status.
SEC #2
(B)
DCS #2
(B)
1.4 Check device status
Device
Get device
status
Device status notify
MCC
1. Broadcast notify

## Slide 6
SEC #1
(M)
DCS #1
(M)
The main SEC sends the device status to other SEC & MCC.
SEC #2
(B)
DCS #2
(B)
Device
Get device
status
Device status
MCC
2. Only controlled SEC notify
Device status

## Slide 7
SEC #1
(M)
DCS #1
(M)
Each SEC get device status form DCS.
SEC #2
(B)
DCS #2
(B)
Device
Get device
status
Get device status
MCC
3. Each SEC direct check device status

## Slide 8
2. DCS Redundant configuration
DCS #1
(M)
Periodic check of main DCS's alive status.
If main DCS is deadlocked, backup DCS is switch to main.
Control device by switched to main DCS.
When the previous main DCS is restarted, get all event receive from main DCS and it operates as a backup.
1.1 DCS redundant workflow
DCS #2
(B)
Alive
Alive check
Alive check
Switch main
Dead
Control device
Restart &
switch backup
Get all event
receive

## Slide 9
3. Main/Backup event redundant configuration
SEC
SEC checks the status of the main event device through DCS.
If there is a problem with the device of the main event, exchange the main and backup events..
3.1 Main/Backup redundant workflow
DCS
(B)
Main device
deadlock
DEC #1 (M)
DEC #2 (B)
Main device
check
Exchange
main/backup
event
Device check